## Slide 1: SRAM 设计举例：
现有容量为 8K×8bit 的 SRAM 芯片。
在8086系统中，
（1）利用这样的芯片构成地址范围为C0000H～C7FFFH的内存，画出最大模式下包括总线驱动在内的此芯片与系统总线的连接图（译码器件自行选择）。
（2）试编写8086汇编语言程序，从地址C0000H开始，依次写入数据，直到地址C7FFFH。要求数据从0开始，每写入一个字节后数据加1，即写入数据依次为：00H、01H、02H、03H、……、FEH、FFH、 00H、01H、……。然后逐个单元读出比较，若有错，则在DL中写入01H，退出检测；若每个单元均对，则在DL写入00H。

## Slide 2: SRAM 设计举例：
现有容量为 8K×8bit 的 SRAM 芯片。
构成8086系统内存，地址范围C0000H～C7FFFH。
内存地址分析：
A19 | A18 | A17 | A16 | A15 | A14 | A13 | A12 | A11 | ～ | A4 | A3 | A2 | A1 | A0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | ～ | 0 | 0 | 0 | 0 | 0
 |  |  |  |  |  | 1 | 1 | 1 | ～ | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | ～ | 0 | 0 | 0 | 0 | 0
 |  |  |  |  |  | 1 | 1 | 1 | ～ | 1 | 1 | 1 | 1 | 1
【解】
C8000H－C0000H＝8000H，即32K，则：
需要芯片片数＝32KB/8KB＝4片。
SRAM芯片 地址线：A0～A12 ，数据线：D0～D7
可用3-8译码器实现

## Slide 3
D0～D7
A0～A12
WE
CS
OE
A B
74LS245
DIR
OE
74LS244×3片
E2
E1
D0～D7
A1～A13
MEMR
MEMR
MEMW
D’0～D’7
A’1～A’13
MEMR’
MEMW’
D’0～D’7
A’1～A’13
MEMR’
MEMW’
≥1
A’0
D0～D7
A0～A12
WE
CS
OE
D’8～D’15
A’1～A’13
MEMR’
MEMW’
≥1
BHE’
Y0
D0～D7
A0～A12
WE
CS
OE
D’0～D’7
A’1～A’13
MEMR’
MEMW’
≥1
A’0
D0～D7
A0～A12
WE
CS
OE
D’8～D’15
A’1～A’13
MEMR’
MEMW’
≥1
BHE’
Y1
&
CS1
CS3
A B
74LS245
DIR
OE
D8～D15
MEMR
D’8～D’15
&
CS2
CS4
BHE’
A’0
BHE
A0
CS1
CS3
CS2
CS4
A Y
&
&
A19
A18
A17
MEMR’
MEMW’
A16
A15
A14
G1
G2A
G2B
C
B
A
Y0
Y1
Y0
Y1
74LS138
8
0
8
6
总
线
译码
双向驱动
单向驱动
8K×8bit SRAM

## Slide 4
双向数据总线驱动控制电路 及单向信号驱动电路
P129，
图4.21：

## Slide 5
START: MOV AX,0C000H
MOV DS,AX
MOV DI,0
MOV CX,8000H
MOV AL,0
WRITE: MOV [DI],AL
INC DI
INC AL
LOOP WRITE
MOV SI,0
MOV CX,8000H
MOV AL,0
CHECK: CMP AL,[SI]
JNZ ERROR
INC SI
INC AL
LOOP CHECK
MOV DL,0
JMP NEXT
ERROR: MOV DL,1
NEXT: ……
参考程序
START: MOV AX,0C000H
MOV DS,AX
MOV DI,0
MOV CX,4000H
MOV AX,0100H
WRITE: MOV [DI],AX
ADD DI,2
ADD AH,2
ADD AL,2
LOOP WRITE
MOV SI,0
MOV CX,4000H
MOV AX,0100H
CHECK: CMP AX,[SI]
JNZ ERROR
ADD SI,2
ADD AH,2
ADD AL,2
LOOP CHECK
MOV DL,0
JMP NEXT
ERROR: MOV DL,1
NEXT: ……
方案2:
16位写
方案1:
8位写